## Slide 1: DSIP – Lecturer 12 Image Enhancement in the Spatial Domain Neighbourhood Operations

## Slide 2: Neighbourhood Operations
7/30/2020
2
Neighbourhood operations simply operate on a larger neighbourhood of pixels than point operations
Neighbourhoods are mostly a rectangle around a central pixel
Any size rectangle and any shape filter are possible
Origin
x
y
Image f (x, y)
(x, y)
Neighbourhood
Notes: 2

## Slide 3: Local Enhancement through Spatial Filtering
7/30/2020
3
The output intensity value at (x,y) depends not only on the input intensity value at (x,y) but also on the specified number of neighboring intensity values around (x,y)
Spatial masks (also called window, filter, kernel, template) are used and convolved over the entire image for local enhancement (spatial filtering)
The size of the mask determines the number of neighboring pixels which influence the output value at (x,y)
The values (coefficients) of the mask determine the nature and properties of enhancing technique

## Slide 4: Simple Neighbourhood Operations
7/30/2020
4
Some simple neighbourhood operations include:
  Min: Set the pixel value to the minimum in the neighbourhood
  Max: Set the pixel value to the maximum in the neighbourhood
  Median: The median value of a set of numbers is the midpoint value in that set (e.g. from the set [1, 7, 15, 18, 24] 15 is the median). Sometimes the median works better than the average
Notes: 4

## Slide 5: Simple Neighbourhood Operations Example
7/30/2020
5
123
127
128
119
115
130
140
145
148
153
167
172
133
154
183
192
194
191
194
199
207
210
198
195
164
170
175
162
173
151
Original Image
x
y
Enhanced Image
x
y
Notes: 5

## Slide 6: The Spatial Filtering Process
7/30/2020
6
r
s
t
u
v
w
x
y
z
Origin
x
y
Image f (x, y)
eprocessed = v*e + r*a + s*b + t*c + u*d + w*f + x*g + y*h + z*i
Filter
Simple 3*3 Neighbourhood
e
3*3 Filter
a
b
c
d
e
f
g
h
i
Original Image Pixels
*
The above is repeated for every pixel in the original image to generate the smoothed image
Notes: 6

## Slide 7: Local Enhancement through Spatial Filtering
7/30/2020
7

## Slide 8: Basics of Spatial Filtering
7/30/2020
8
Given the 3×3 mask with coefficients: w1, w2,…, w9
The mask covers the pixels with gray levels: z1, z2,…, z9
z gives the output intensity value for the processed image (to be stored in a new array) at the location of z5 in the input image

## Slide 9: Basics of Spatial Filtering
7/30/2020
9
Mask operation near the image border
Problem arises when part of the mask is located outside the
image plane; to handle the problem:
1. Discard the problem pixels (e.g. 512x512input 510x510output, if mask size is 3x3)
2. Zero padding: expand the input image by padding zeros (512x512input 514x514output)
  – Zero padding is not good; creates artificial lines or edges on the border
3. We normally use the gray levels of border pixels to fill up the expanded region (for 3x3 mask). For larger masks a border region equal to half of the mask size is mirrored on the expanded region.

## Slide 10: Mask Operation Near the Image Border
7/30/2020
10

## Slide 11: Spatial Filtering for Smoothing
7/30/2020
11
For blurring/noise reduction;
Blurring is usually used in preprocessing steps,
e.g., to remove small details from an image prior to object extraction, or to bridge small gaps in lines or curves
Equivalent to Low-pass spatial filtering in frequency domain because smaller (high frequency) details are removed based on
neighborhood averaging (averaging filters)
Implementation: The simplest form of the spatial filter for averaging is a square mask (assume m×m mask) with the same coefficients 1/m2 to preserve the gray levels (averaging).
Applications: Reduce noise; smooth false contours
Side effect: Edge blurring

## Slide 12: Smoothing Filters
7/30/2020
12

## Slide 13: Smoothing Spatial Filters
7/30/2020
13
One of the simplest spatial filtering operations we can perform is a smoothing operation
  Simply average all of the pixels in a neighbourhood around a central value
  Especially useful in removing noise from images
  Also useful for highlighting gross detail
1/9 | 1/9 | 1/9
1/9 | 1/9 | 1/9
1/9 | 1/9 | 1/9
Simple Averaging Filter
Notes: 13

## Slide 14: Smoothing Spatial Filtering
7/30/2020
14
1/9
1/9
1/9
1/9
1/9
1/9
1/9
1/9
1/9
Origin
x
y
Image f (x, y)
e = 1/9*106 + 1/9*104 + 1/9*100 + 1/9*108 + 1/9*99 + 1/9*98 + 1/9*95 + 1/9*90 + 1/9*85
= 98.3333
Filter
Simple 3*3 Neighbourhood
106
104
99
95
100
108
98
90
85
1/9
1/9
1/9
1/9
1/9
1/9
1/9
1/9
1/9
3*3 Smoothing Filter
104
100
108
99
106
98
95
90
85
Original Image Pixels
*
The above is repeated for every pixel in the original image to generate the smoothed image
Notes: 14

## Slide 15: Spatial Filtering for Smoothing (Example)
7/30/2020
15

## Slide 16: Spatial Filtering for Smoothing (Example)
7/30/2020
16

## Slide 17: Weighted Smoothing Filters
7/30/2020
17
More effective smoothing filters can be generated by allowing different pixels in the neighbourhood different weights in the averaging function
  Pixels closer to the central pixel are more important
  Often referred to as a weighted averaging
1/16 | 2/16 | 1/16
2/16 | 4/16 | 2/16
1/16 | 2/16 | 1/16
Weighted Averaging Filter
Notes: 17

## Slide 18: Order-Statistics Filtering
7/30/2020
18
Nonlinear spatial filters
Output is based on order of gray levels in the masked area (sub-image)
Examples: Median filtering, Max & Min filtering
Median filtering
Assigns the mid value of all the gray levels in the mask to the center of mask;
Particularly effective when
  – the noise pattern consists of strong, spiky components (impulse noise, salt-and-pepper)
  – edges are to be preserved
  – Force points with distinct gray levels to be more like their neighbors

## Slide 19: Median Filtering
7/30/2020
19

## Slide 20: Median Filtering (Example)
7/30/2020
20

## Slide 21: Overcoming the Edges Problems
7/30/2020
21
Origin
x
y
Image f (x, y)
e
e
e
e
At the edges of an image we are missing pixels to form a neighbourhood
e
e
e
Notes: 21

## Slide 22: Overcoming the Edges Problems
7/30/2020
22
There are a few approaches to dealing with missing edge pixels:
  Pad the image
    Typically with either all white or all black pixels
  Replicate border pixels
  Truncate the image
Notes: 22

## Slide 23: Simple Neighbourhood Operations Example
7/30/2020
23
123
127
128
119
115
130
140
145
148
153
167
172
133
154
183
192
194
191
194
199
207
210
198
195
164
170
175
162
173
151
x
y
Notes: 23

## Slide 24: Correlation & Convolution
7/30/2020
24
The filtering we have been talking about so far is referred to as correlation with the filter itself referred to as the correlation kernel
Convolution is a similar operation, with just one subtle difference
For symmetric filters it makes no difference
eprocessed = v*e + z*a + y*b + x*c + w*d + u*e + t*f + s*g + r*h
r
s
t
u
v
w
x
y
z
Filter
a
b
c
d
e
e
f
g
h
Original Image Pixels
*
Notes: 24

## Slide 25: Spatial Filtering for Image Sharpening
7/30/2020
25
Background: to highlight fine detail in an image or to enhance blurred detail
Applications: electronic printing, medical imaging, industrial inspection, autonomous target detection (smart weapons)......
Foundation (Blurring vs Sharpening):
Blurring/smoothing is performed by spatial averaging (equivalent to integration)
Sharpening is performed by noting only the gray level changes in the image that is the differentiation

## Slide 26: Spatial Filtering for Image Sharpening
7/30/2020
26
Operation of Image Differentiation
Enhance edges and discontinuities (magnitude of output gray level >>0)
De-emphasize areas with slowly varying gray-level values (output gray level: 0)
Mathematical Basis of Filtering for Image Sharpening
First-order and second-order derivatives
Gradients
Implementation by mask filtering

## Slide 27: Derivatives
7/30/2020
27
First Order Derivative
A basic definition of the first-order derivative of a one-dimensional function f(x) is the difference
Second Order Derivative
Similarly,the second-order derivative of a one-dimensional function f(x) is the difference

## Slide 28: First and Second Order Derivatives
7/30/2020
28

## Slide 29: Example for Discrete Derivatives
7/30/2020
29

## Slide 30: Comparison between f" and f´
7/30/2020
30
f´ generally produces thicker edges in an image
f" has a stronger response to fine detail
f´ generally has a stronger response to a gray-level step
f" produces a double response at step changes in gray level
For image enhancement, f" is generally better suited
than f´
Major application of f´ is for edge extraction; f´ used together with f" results in impressive enhancement effect

## Slide 31: Laplacian for Image Enhancement
7/30/2020
31

## Slide 32: Laplacian for Image Enhancement
7/30/2020
32

## Slide 33: Laplacian for Image Enhancement
7/30/2020
33

## Slide 34: Laplacian for Image Enhancement (Example)
7/30/2020
34

## Slide 35: Laplacian for Image Enhancement (Example)
7/30/2020
35

## Slide 36: Image Sharpening Based on Unsharp Masking
7/30/2020
36

## Slide 37: High Boost Filtering
7/30/2020
37
Principal application:
Boost filtering is used when input image is darker than desired,
high-boost filter makes the image lighter and more natural

## Slide 38: High Boost Filtering Masks
7/30/2020
38

## Slide 39: 1st Derivative Filtering
Implementing 1st derivative filters is difficult in practice
For a function f (x, y) the gradient of f at coordinates (x, y) is given as the column vector:
Notes: 39

## Slide 40: 1st Derivative Filtering (cont…)
The magnitude of this vector is given by:
For practical reasons this can be simplified as:
Notes: 40

## Slide 41: 1st Derivative Filtering (cont…)
Now we want to define digital approximations and their Filter Masks
For simplicity we use a 3x3 region
For example z5 denotes f(x,y), z1 denotes f(x-1,y-1)
A simple approximation for First Derivative is
z1
z2
z3
z4
z5
z6
z7
z8
z9

## Slide 42: 1st Derivative Filtering (cont…)
A simple approximation for First Derivative is
z1
z2
z3
z4
z5
z6
z7
z8
z9
Two other definitions proposed by Roberts use cross- difference
If we use

## Slide 43: 1st Derivative Filtering (cont…)
z1
z2
z3
z4
z5
z6
z7
z8
z9
If we use absolute values then
The Masks corresponding to these equations are:
Roberts Cross-Gradient Operators

## Slide 44: Gradient Operators
7/30/2020
44

## Slide 45: Gradient Operators
7/30/2020
45
Normally the smallest mask used is of size 3 x 3
Based on the concept of approximating the gradient several spatial masks have been proposed:

## Slide 46: Gradient Operators
7/30/2020
46

## Slide 47: Gradient Processing (Example)
7/30/2020
47

## Slide 48: NOTE
7/30/2020
48
The summation of coefficients in all masks equals 0, indicating that they would give a response of 0 in an area of constant gray level.

## Slide 49: Mask used to estimate the Gradient

## Slide 50: Combining Spatial Enhancement Methods (cont…)
Laplacian filter of bone scan (a)
Sharpened version of bone scan achieved by subtracting (a) and (b)
Sobel filter of bone scan (a)
(a)
(b)
(c)
(d)
Notes: 50

## Slide 51: Combining Spatial Enhancement Methods (cont…)
The product of (c) and (e) which will be used as a mask
Sharpened image which is sum of (a) and (f)
Result of applying a power-law trans. to (g)
(e)
(f)
(g)
(h)
Image (d) smoothed with a 5*5 averaging filter
Notes: 51

## Slide 52: Combining Spatial Enhancement Methods (cont…)
Compare the Original and Final Images
Notes: 52