## Slide 1: Lecture - 25 Discrete Time Signal and Systems – Revision

## Slide 2: Discrete-Time Systems
  Discrete-Time Systems
  Block Diagram Representation
  Difference Equations
  Classification of Discrete-Time Systems
    Static Systems
    Time-invariant Systems
    Linear Systems
    Causal Systems
    Stable Systems
  Linear Time-Invariant Discrete (LTD) systems
    Impulse response of a LTI System
    Finite Impulse Response (FIR) System
    Infinite Impulse Response (IIR) System
    Convolution
  Stability of LTD Systems
  Problem Sheet A2

## Slide 3: 2 : Discrete-Time Systems
2.1 Discrete-Time System
A discrete - time system is a device or algorithm that operates on a discrete-time signal called the input or excitation according to some well defined rule, to produce another discrete-time signal called the output or response.
We say that the input signal x[n] is transformed by the system into a signal y[n], and express the general relationship between x[n] and y[n] as
(2.1)
yn Hxn

## Slide 4: yn H xn
H
x[n]
y[n]
Figure 2.1. Block diagram representation of a discrete-time System
where the symbol H denotes the transformation or processing performed by the system on x[n] to produce y[n] (see Fig 2.1)
x[n] y[n]
H
(2.1)

## Slide 5: 2.2 Block Diagram Representation
In order to introduce a block diagram representation of discrete-time systems, we need to define some basic blocks that can be interconnected to form complex systems.
  An adder : A system that performs the addition of two signal sequences to form another sequence, which we denote as y[n].
Note: It is not necessary to store either one of the sequences in order to perform the addition. In other words, the addition operation is memoryless.

## Slide 6
x1[n]
+
x2[n]
y[n] = x1[n]+x2[n]
x1[n] = {4, 5, -3}
x1[0]
x1[2]
sequence
at n=0 n=2
9, 0}
n=0 n=1 n=2
y[0]
y[2]
x2[n] = {-2, 4, 3}
n=0 n=2
Figure 2.2. Block diagram representation of an adder, x1[n] and x2[n] denote discrete-time input signals and y[n] denote a discrete-time output signals.

## Slide 7: (b) A constant multiplier: This operation simply represents applying a scale factor on the input x[n]. Note that this operation is also
a
memoryless.
multiplier
x[n]
y[n] = ax[n]
Figure 2.3. Block diagram representation of a multiplier. x[n] and y[n] denote discrete-time input and output signals respectively. a denotes a scalar multiplier.

## Slide 8: sequence
x[n] = {2, -5, 6, 8}; a = 0.1; y[n] ={0.2, -0.5, 0.6, 0.8}
at n=0 n=3 at n=0 n=3
(c) A Unit Delay Element : The unit delay is a special system that simply delays the signal passing through it by one sample.
If the input signal is x[n], the output is x[n-1]. In fact, the sample x[n-1] is stored in memory at time n-1 and
it is recalled from memory at time n to form y[n] = x[n-1].
Thus this basic building block requires memory

## Slide 9
The use of symbol T or z-1 to denote the unit of delay.
T
x[n]
y[n] = x[n-1]
Figure 2.4. Block diagram representation of a unit delay. T denotes the sampling period.

## Slide 10: Example:
Z-1
x[n]
y[n] = x[n-1]
unit delay
y[n] =
at n= -1; n=0; n=1
x[n] = {0, 1, 0, 5, 7, -2, -1, 0}
{0, 1, 0, 5, 7 , -2, -1}
y[0] y[1] y[2] … y[6]
{ y[n] = x[n-1]; y[0]=x[0-1]=x[-1]; y[1] = x[1-1]=x[0];…}

## Slide 11: Note: Normally a combination of adders, multipliers and unit delays form a complex discrete-time system.

## Slide 12
-20
-15
-10
-5 0
5
10
15
20
0
0.5
1
unit step
-20
-15
-10
10
15
20
0
0.5
1
unit step shifted left
-20
-15
-10
-5
0
5
10
15
20
0
0.5
1
-5 0 5
unit step shifted right

## Slide 13: 2.3 Difference Equations
A discrete-time system consisting of combinations of adders, multipliers and unit delays can always be described by a set of difference equations. The equations would be ordinary algebraic equations if no delays were present.

## Slide 14: Examples:
(a) y[n] = x[n-2]
T
x[n]
x[n-1]
T
y[n] = x[n-2]
T - Unit sample delay sampling period

## Slide 15: (b) y[n]  1 x[n]  1 x[n 1]  1 x[n  2] 2 4 4
T
x[n]
x[n-1]
T
x[n-2]
+
y[n]
0.5
0.25
0.25
0.5 x[n]

## Slide 16: (c) yn  xn 0.25 yn  1
y[n]
y[n-1] | T | 
+
0.25
x[n]
4
(d) y[n]   x[n  k]  x[n]  x[n 1]  x[n  3]  x[n  4]
k 0

## Slide 17: Example:
yn a0xn a1xn 1 b1y[n 1]
Draw a system implementation for the above difference equation.
y[n]
x[n]
a0
System 2
+
T
-b1
+
T
a1
v[n]
Feedforward Part Feedback Part Figure 2.5. Direct Form I structure
System 1

## Slide 18
We can write the above difference equation as a set of two equations

- system 1

- system 2
y[n]
x[n]
a0
System 2
+
T
-b1
+
T
a1
v[n]
Feedforward Part Feedback Part Figure 2.5. Direct Form I structure
System 1
yn  vn b1 yn  1
vn a0 xn a1xn 1

## Slide 19: y[n]
System 1 |  | System 2
v[n]
x[n]
System 2 |  | System 1
p[n]
x[n]
y[n]
Cascade structure
Figure 2.6. Two systems forming a cascade structure can be interchanged without affecting the final output signal.
Without changing the input-output relationship, we can reverse the ordering of the two systems in the cascade representation.

## Slide 20: 2.4 Classification of Discrete- Time Systems
In the analysis as well as in the design of systems, it is desirable to classify the systems according to the general properties that they satisfy. For a system to possess a given property, the property must hold for every possible input signal to the system. If a property holds for some input signals but for others, the system does not possess the property.

## Slide 21
General Categories are:
  Static systems
  Time - invariant systems
  Linear systems
  Causal systems
  Stable systems

## Slide 22
    Static Systems
      A discrete-time system is called static or memoryless if its output at any instant ‘n’ depends at most on the input sample at the same time, but not on past or
future samples of the input.
Example:
yn  axn
yn  nxn bx3 n
N
yn   xn  k 
k 0
Both are static or memoryless.
On the other hand, the systems described by the following input-output relations, such as
yn  xn 3xn  1
are dynamic systems or system with memory.

## Slide 23: 2.4.2 Time-invariant systems
A time-invariant system is defined as follows:
xn  n0 ⎯⎯ yn  n0 
H
where y[n] = H{x[n]}.
Specifically, a system is time invariant if a time shift in the input signal results in an identical time shift in the output signal.

## Slide 24: yn H xn nxn
Example: Determine if the system is time variant or time invariant.
This system is time variant, since
(2.7)
The response of this system to x[n-k] is
wn  nxn  k 
Now if we delay y[n] in (2.7) by k units in time, we obtain
yn  k   n  k xn  k 
 nxn  k  kxn  k 
yn  k  wn

## Slide 25: 2.4.3 Linear Systems
A linear system is defined as follows:
where a1 and a2 are arbitrary constants.
(2.8)
1 1 2 2
1 1 2 2
H
 a y n a y n
a x n a x n⎯⎯

## Slide 26: Example: Three sample averager
3
1 2
1 2
 ax1n bx2n
 ax1n 1 bx2n 1}
 [ay1n by2n]
H{ax n bx n}  1{ax n 1 bx n 1
3
xn⎯⎯H  yn
yn  1 xn 1 xn xn 1  H xn
The 3-sample averager is a linear system.

## Slide 27: yn   H xn   x 2 n 
Example:
n x n 
2
1
2
2 2
1
2 2
2
1 2
2
1
n  2 abx 
n  b x 
  ax n  bx n 
 a x 
H ax n  bx n 
which is not equal to ax 
2
2
2
1
n bx n
This system is nonlinear.

## Slide 28: Example :
yn  nxn  H  xn  H  ax1n bx 2 n  anx1n bnx 2 n
 ay1n by 2 n
The system is linear.

## Slide 29: 2.4.4 Causal systems
A system is said to be causal if the output of the system at any time ‘n’ depends only on present and past inputs, but does not depend on future inputs.
If a system does not satisfy this definition, it is called noncausal. Such a system has an output that depends not only on present and past inputs but also on future inputs.

## Slide 30: Example :
 Noncausal
 Causal
 Causal
yn  x n
yn  xn 3xn  4 Noncausal
yn  axn
yn  xn xn  1
{Let n = -1  y[-1]= x [1], the output at
n = -1 depends on the input at n = 1.}

## Slide 31
Discrete - time sequence is called
causal if it has zero values for n<0.
y[n]
Causal
& Stable
n
Figure 2.9. An example of causal discrete-time sequence.
n
3
2
yn    un

## Slide 32: 2.4.5 Stable Systems
A discrete signal x[n] is bounded if there exists a finite M such that
|x[n]| < M for all n.
A discrete - time system in Bounded Input-Bounded Output (BIBO) stable if every bounded input sequence x[n] produced a bounded output sequence.
If xnmax  A, then ynmax  B

## Slide 33: Example:
The discrete - time system
yn  nyn 1 xn, n  0
is at rest [i.e. y[-1]=0]. Check if the system is BIBO stable.

## Slide 34: n  0  y0  x0  1
If x[n]=u[n], then |x[n]|  1. But for this bounded input, the output is
n  1  y1  1y0 x1  2
n  2  y2  2 y1 x2  5
M M
Which is unbounded. Hence the system is unstable.

## Slide 35: 2.5 Linear Time-Invariant Discrete (LTD) Systems
Transformation of Discrete-Time signals :
A discrete-time signal, x[n] may be shifted in time (delayed or advanced) by replacing the variables n with n-k where k > 0 is an integer
x[n-k] => x[n] is delayed by k samples
x[n+k] => x[n] is advanced by k samples

## Slide 36:  yn xn n  k  xk  n  k 
For example consider a shifted version of the unit impulse function (see Figure 2.10). If we multiply an arbitrary signal x[n] by this function, we obtain a signal that is zero everywhere, except at n = k.
(2.9)
[n-k]
1
0 1 2 k-1 k k+1
n
0 1 2 k-1 k k+1
1
x[n]
n
y[n]
1
0 1 2 k-1 k k+1
n
Figure 2.10. Multiplying a discrete-time signal, x[n], with a shifted unit impulse function, [n-k], produces a discrete- time signal whose sample is zero except at n=k.

## Slide 37
Figure 2.11. An example of expressing arbitrary discrete-time sequences as a sum of scaled and delayed unit impulses.
n
a-3
a1
An arbitrary sequence can then be expressed as a sum of scaled and delayed unit impulses.
p[n]
a4
-3 -2 -1 0 1 2 3 4 5 6 7
a2 a7
p[n] = a-3[n+3] + a1[n-1] + a2 [n-2] + a4 [n-4]+ a7-[n-7]

## Slide 38
More generally, the discrete-time sequence can be expressed according to
For real time signals
and for a real-time signal with a finite number of
samples N.
(2.10)

xn  xk  n  k 
k 

xn   xk  n  k 
k 0
(2.11)
N 1
xn  xk  n  k 
k 0

## Slide 39
If x[n] has finite duration, the infinite sum in equation (2.11) may be replaced by a finite sum.
That is if x[n]  0 for –N2  n  N1,
N1
xn  xk  n  k 
k  N 2
0
x[n]
N2
N1 n
Figure 2.12. An example of finite duration discrete-time sequences.

## Slide 40
Equation (2.11) is a special form of convolution. Generally, the convolution of two sequences x[n] and y[n] is defined as
convolution is commutative:
ie. x[n] * y[n] = y[n] * x[n]
(2.12)

  xn  k yk 
k 
convolution
xn * yn  xk yn  k 
k 


## Slide 41: 2.5.1 The impulse Response of a LTI system
For example consider the discrete-time system, H, shown in Figure 2.13
Figure 2.13. An example of discrete-time system, whose input and output are represented by x[n] and y[n], respectively.
x[n]
T
a
b
T
System H
y[n]
v[n]
c
+
+

## Slide 42
Difference equation for the system H :
vn axn bxn 1 yn
y[n]  cv[n 1] (2.13)
From the above difference equations, y[n] can be determined for a given input.
x[n]
T
a
b
T
System H
y[n]
v[n]
c
+
+

## Slide 43: x[n] = [n]
Let
Unit impulse
Assume v[n] = 0 for n 0  y[n] is also initially zero for n  0. Substituting n = 0,1,2,... in equation (2.13), we obtain
n = 0
v[0]=ax[0]+bx[-1]+y[0]=
a1+b0+0=a
 y[1] = ac
n = 1
v[1] = ax[1] + bx[0] + y[1] =
a0 + b1+ ac= b+ac
 y[2] = cv[1] = c(b+ac)

## Slide 44
n = 2
v[2] = ax[2] + bx[1] + y[2] =
0 + 0 + c(b+ac)
 y[3] = cv[2] = c2(b+ac)
...
n = n – 1
v[n-1] = bcn-2 + acn-1
 y[n] = c v[n-1] = bcn-1 + acn
 yn xn n  hn bc  ac
n1 n
Impulse response

## Slide 45: n hn
to an impulse excitation
(x[n] =  [n]) is known as the impulse response and it is a very important characteristic of a discrete system.
If x[n] = [n], then y[n] = h[n]. The output tells us the system behaviour as the system is being hit by all input frequencies. h[n] completely characterizes the system.
The response y
Δ
H
x[n]
y[n]

## Slide 46: [n]
We have
and since the system is time invariant, the response
to [n-k] must be h[n-k]
Therefore
h[n]
H
[n-k]
h[n-k]
H
x[k][n-k]
x[k]h[n-k]
H

## Slide 47
Now recall that each x[n] can be written as a weighted sum of shifted unit impulse (see equation (2.10)). Therefore
 
 x[k ] [n  k ] ⎯⎯H   x[k ]h[n  k ]
k  k 
x[n] x[n] * h[n] (see equation (2.12))
and
xn⎯⎯H  yn  xn* hn

## Slide 48
The response to an arbitrary input signal x[n] is the convolution of x[n] with the impulse response of the
system.
H
x[n]
y[n]
System H:
impulse response of the system
yn xn* hn (2.15) |  | 
 yn  xn* hn   xk hn  k  k  |  | 
 yn hn* xn  hk xn  k  (2.16) k  |  | 
where h[n]=H{[n]}.

## Slide 49: 2.5.2 Finite Impulse Response (FIR) System
If the impulse response of a LTI system is of finite duration, the system is said to be Finite Impulse Response (FIR).
 1
2
n
x[n] = [n]
2
Impulse Response
x[n] = [n]
n
0 1 2
Input
Non-recursive system
x[n]
y[n]
Figure 2.14. An example of LTI systems with finite impulse response.
T
-1/2
2
+

## Slide 50: x[n] = [n]
n = 0
n = 1
n = 2
y[n] = 2x[n] - 0.5x[n-1]
y[0] = h[0] = 2x[0] – 0.5x[-1] = 2
y[1] = h[1] = 2x[1] – 0.5x[0] = -0.5
y[2] = h[2] = 2x[2] – 0.5x[1] = 0
n = n
0

## Slide 51: 2.5.3 Infinite Impulse response (IIR) system
If the impulse response of a linear time-invariant system is of infinite duration, the system is said to be an Infinite Impulse Response (IIR) system.
x[n] = [n]
recursive system
x[n]
y[n]
v[n]
1
+ T
0 1 2 n
Input
Figure 2.15. An example of discrete systems with infinite impulse response.

## Slide 52: vn  xn yn
yn  1.vn 1
If x[n] = [n], calculate h[n]
for n=0,1,2,...

## Slide 53: Example:
Find the impulse response h[n] of the following first- order recursive system.
To find h[n], we let x[n] = [n] and apply the zero initial condition.
⎩
⎨
⎧
0
n  0 otherwise
ayn 1 xn
yn 

## Slide 54: n = 0, y[0] = h[0] = ay[-1] + [0] = 1 n = 1, y[1] = h[1] = ay[0] + [1] = a
n = 2, y[2] = h[2] = ay[1] + [2] = a2
n = n, y[n] = h[n] = an
for n  0
y[n] = h[n] = 0 for n < 0, because [n] is zero for n < 0 and
y[-1]= 0.

## Slide 55
Hence, h[n]=anu[n] for all n
h[n]
0 < a < 1
1
0
n
h[n]
a > 1
1
0
n
h[n]=anu[n]
y[n]
x[n]
y[n]
x[n]
T
a

y[n] = x[n] * h[n]
+

## Slide 56: Example:
Find the impulse response h[n] of the following fourth order non-recursive system.
yn  a0 n a1xn 1 a2 xn  2
a3xn  3 a4 xn  4
To find h[n], we let x[n] = [n].

## Slide 57: h[0] = a0[0] +a1[-1]+a2[-2]+ a3[-3] +a4[-4] = a0
n=0
n=1 h[1] = a0[1] + a1[0] + a2[-1]+
a3[-2]+a4[-3] = a1
n=2 h[2] = a0[2] + a1[1] + a2[0] +
a3[-1] + a4[-2]= a2
n=3 h[3] = a0[3] + a1[2] + a2[1] + a3[0] + a4[-1] = a3
n=4
h[4] = 0 + 0 + 0 + 0 + a4[0] = a4
n=5
h[5] = 0 + 0 + 0 + 0 + a4[1] = 0

## Slide 58
For n  5, h[n] = 0, since the nonzero value of [n]
has moved out of the memory of this system.
[n]
 |  | T |  |  | T |  |  | T |  |  | T | 
+
x[n]
y[n]=h[n]
h[n]
a
0
a1
a2
a3
a4
a0, a1, a2, a3 & a4 are called coefficients (+ or -) or constants

## Slide 59: Example:
Two structures are shown below:
  Write the difference equation
  Calculate the impulse response
x[n]
T
T
y[n]
+
1
1
1
x[n]
T
T
y[n]
+
1
1
1

## Slide 60
Structure 1 :
y[n] = x[n] + x[n-1] + x[n-2]
h[n]=y[n]|x[n] =[n]
h[n] = [n] + [n-1] + [n-2]
h[0]=1; h[1] = 1; h[2] = 1 and h[n] = 0 n  3
x[n]
T
T
y[n]
1
1
1
+

## Slide 61
Structure 2 :
y[n] = x[n] - x[n-2]
h[n]=y[n]|x[n] =[n]
h[n] = [n] - [n-2]
h[0]=1; h[1] = 0; h[2] = -1 and h[n] = 0 n  3
T
T
x[n]
y[n]
+1
-1
+

## Slide 62: yn  xn* hn   xk hn  k 
2.5.4 Convolution

k 

yn hn* xn  hk xn  k 
k 
Commutative Law:
xn* hn  hn* xn
Associative Law:
xn* h1n* h2 n  xn* h1n* h2 n

## Slide 63: y[n] 
h1[n]
h2[n]
x[n]
h2[n]
h1[n]
y[n]
y[n]  x[n]
h1[n]
h2[n]
x[n]
h[n]= h1[n]*h2[n]
y[n]
x[n]

## Slide 64: Distributive Law:
xn* h1n* h2n  xn* h1n xn* h2n
x[n]
h1[n]
h2[n]
h[n]= h1[n]+ h2[n]
y[n]
y[n]
+  x[n]

## Slide 65: Graphical computation of convolution.
The convolution of two signals x[n] and h[n] is shown in steps in the diagram below.
h[n] x[n]
1
i
0 1 2 3 4 n
h[-i]
1
Step 1: Fold h[i] over in time; this gives h[-i].
i

## Slide 66
Step 3:
Multiply x[i] by h[n-i]
x[i]h[2-i]
1
0 1 2 3 4 5 i
Step 2:
Shift h[-i] through a distance n, This gives h[n-i].
We have chosen n=2 in the diagram.
h[2-i]
1
0 1 2 3 4 5 i

## Slide 67: y[n] 1
Step 5:
Vary n from - to . This gives y[n].
Step 4:
Sum this product over all i. This gives the signal value y(2),
0 1 2 3 4 5 i
y[n]
y[2]
0 1 2 3 4 5 n

y2   xih2  i
i  

## Slide 68: Exercise :
Compute the convolution y[n] = x[n] * h[n] of the following pair of signals, using
  Equation (2.16)
  Graphical computation.
x[n]
0.5
n
2
-4 -3 -2 -1
h[n]
0 1 2 3 4 n
3
2
1

## Slide 69: Answer :
1.5
0 1 2 3 4 5 n
y[n]=x[n]*h[n]
3.0
2.5
1.5
0.5

## Slide 70
% Exercise 3. Convolution &
% filtering
%
% Matlab has a built-in function
% to perform convolution, which
% is called `conv'.
% Use `help' command to find out
% more about `conv'.
%
% We now evaluate the sequences
% x, h and y from the previous
% example.
sequence_x = [zeros(1,4) ones(1,3)*0.5 zeros(1,3)]
sequence_h = [zeros(1,4) 3:-1:1 zeros(1,3)]
sequence_y = conv (sequence_x, sequence_h);
discrete_time = -4:5;

## Slide 71
% Plot the sequences
figure
subplot(3,1,1)
plot(unit_step)
stem(discrete_time, sequence_x)
axis([-5 5 0 1])
title ('x[n]')
subplot(3,1,2)
stem(discrete_time, sequence_h)
axis([-5 5 0 3])
title('h[n]')
subplot(3,1,3)
extended_discrete_time = - 8:10;
stem(extended_discrete_time, sequence_y)
axis([-5 5 0 3])
title('y[n]')
-5
-4
-3
-2
-1
1
2
3
4
5
0
0.2
0.4
0.6
0.8
1
x[n]
-5
-4
-3
-2
-1
1
2
3
4
5
0
1
2
3
0
h[n]
-5
-4
-3
-2
-1
0
1
2
3
4
5
0
1
2
3
0
y[n]

## Slide 72: Example:
Determine the impulse response for the cascade of two linear time-invariant systems having impulse response.
n
n
⎝ ⎠
⎝ ⎠
⎜ 4 ⎟
and h n  ⎛ 1 ⎞ un
⎜ 2 ⎟
h n  ⎛ 1 ⎞ un
2
1
h1[n]
h2[n]
y[n]
x[n]
p[n]

## Slide 73
h[n]
y[n]
y[n] = p[n] * h2[n] and p[n]=x[n]*h1[n]
= (x[n] * h1[n]) * h2[n]
= x[n] * (h1[n] * h2[n]),
{using associative law: h1[n] * h2[n] =h[n]}
x[n]

## Slide 74:  h1n* h2n  h1k h2n  k 
1
1
⎟ (2 1)
⎝ 4 ⎠
2  ⎜
⎟
⎝ 4 ⎠
⎛ ⎞
 ⎜
⎜ ⎟ ⎜ ⎟
⎟
⎞
⎝ 4 ⎠
⎜






n1
⎛ 1 ⎞n
n
k 0
k
n
n
k 0 ⎝ 2 ⎠ ⎝ 4 ⎠
⎛ 1 ⎞k ⎛ 1 ⎞nk
k 0 ⎝ 2 ⎠
nk
⎛ 1 ⎞k ⎛
k 
un  k  
⎟ uk ⎜
hn
⎟ ⎥
⎟ ⎢2  ⎜
⎝ 2 ⎠ ⎢⎣
n  0
⎝ 2 ⎠ ⎥⎦
for
h[n]  0
for n  0
hn ⎜
⎛ 1 ⎞n ⎤
⎛ 1 ⎞n ⎡

## Slide 75
2
2
1
2
2
2
4
2
2
4
1
⎝ ⎠ ⎥⎦
⎝ ⎠ ⎢⎣
 ⎜ ⎟ ⎢2  ⎜ ⎟ ⎥
2 2
1 1
⎜ ⎟
⎝ ⎠
1
⎟
⎝ 2 ⎠
⎛ ⎞
 ⎜
⎠
⎜ ⎟
⎜ ⎟
⎝ ⎠


⎠ ⎝ ⎠
⎜ ⎟ ⎜ ⎟
⎜ ⎟
⎝ ⎠


⎠ ⎝ ⎠
⎜ ⎟ ⎜ ⎟

⎟
⎞
⎝ 2 ⎠
⎜







n  0
for
un  k 
⎟ uk ⎜
⎛ 1 ⎞n ⎤
⎛ 1 ⎞n ⎡
⎛ 1 ⎞n1
n
n
k 0 ⎝
⎛ 1 ⎞k
⎛ 1 ⎞n
⎛ 1 ⎞k ⎛ 1 ⎞k
n
k 0 ⎝
⎛ 1 ⎞n
n
k 0 ⎝
⎛ 1 ⎞nk
⎛ 1 ⎞k
nk
⎛ 1 ⎞k ⎛
k  ⎝ 4 ⎠
hn  h2n* h1n  h2k h1n  k 
k 
⎟ ⎥un
hn ⎜
⎝ 2 ⎠ ⎥⎦
⎛ 1 ⎞n ⎤
⎟ ⎢2  ⎜
⎝ 2 ⎠ ⎢⎣
⎛ 1 ⎞n ⎡


## Slide 76: Example :
x[n] y[n]
Determine the response of the (relaxed) system characterised by the impulse response
n
⎜ ⎟
⎝ 2 ⎠
hn ⎛ 1 ⎞ un

## Slide 77: yn  hk xn  k 
   
4
4
1
1
4
1
2
1
2
  2
1  1
1   
 2





n 1
 2n
k
 
n

k 0
n
n  k
k
n
k 0
n  k
k
k  
un  k 
u k  2
⎤un
⎥
⎥⎦
⎟
 ⎜
n 1
n 1
⎝ 2 ⎠
⎛ 1 ⎞
yn ⎢2
3 ⎢⎣
2 ⎡

## Slide 78: 2.6 Stability of Linear Time- Invariant Systems [11]
An LTD system is stable if, and only if, the stability factor denoted by S, and defined by
is finite.

S  | hk |  
k 

## Slide 79
Let x[n] be a bounded input sequence
{ie. | x[n]|<M for all n, where M is a finite number}.
We must show that the output is bounded when S is finite. To this end, we work again with the convolution formula.

yn   hk xn  k 
k 

## Slide 80
If we take the absolute value of both sides of the above equation, we obtain
Now, the absolute value of the sum of terms is always less than or equal to the sum of the absolute values of the terms

 hk xn  k 
k 
y[n] 

| xn  k |
| yn| | hk |
k 

## Slide 81
Since the input values are bounded , say by
M, we have for all n:
Hence, since both M and S are finite, the output is also bounded. ie, a LTD system is stable if its impulse response is absolutely summable.

M | hk |  MS
k 
| yn|

## Slide 82
Example:
Check the stability of the first-order recursive system shown below:
yn  ayn 1 xn
The impulse response of this system is:
for all formula
hn anun


 | a |n
k 
S   | hn|
k 

## Slide 83
It is obvious that S is unbounded for |a|  1, since then each term in the series is  1.
For |a| < 1, we can apply the infinite geometric sum formula, to find
Since S is finite for |a| < 1, the system is stable.
for | a | 1
1
1 | a |
S 

## Slide 84: Q4. Draw a system implementation for each of the
following difference equations:
(a) 2 yn yn  1 4 yn  3  xn 3xn  5
(b) yn  xn xn  N 
(c) yn  a0 xn a1xn  1 a2 xn  2 b1 yn  1 b2 yn  2 (d) yn  xn xn  1
(e) yn  xn xn  1
(f) yn  2xn 3xn  1 2xn  2 (g) yn  b1 yn  1 a0 xn a1xn  1

## Slide 85: Summary of Part A Chapter 2
At the end of this chapter, it is expected that you should know:
The definition of a discrete-time system
Basic blocks of a discrete-time system: the adder, multiplier and unit delay
How to draw the block diagram of a discrete-time system given its difference equation
How to write the difference equation of a discrete- time system given its block diagram

## Slide 86
Definition and understanding of convolution (including hand and graphical computation of convolution)
The impulse response of a linear, time-invariant system, and how to calculate it from a difference equation
The difference between an FIR and an IIR system. In particular, that the impulse responses of FIR systems have identical values to the coefficients of the difference equation.
Given the impulse responses of two cascaded systems, be able to compute the overall impulse response.

## Slide 87
The difference between Direct Forms I and II and Canonical Form, and how to write a difference equation in all three forms, showing the equivalence between them
The definition (showing proofs and/or examples) of the following types of system:
  Static
  Time Invariant
  Linear
  Causal
  Stable
Interpretation of a discrete time signal as a weighted sum
of delayed impulses