## Slide 1: Lecture - 24 Discrete Time Signal and Systems

## Slide 2: Discrete-Time Systems
  Classification of Discrete-Time Systems
    Static Systems
    Time-invariant Systems
    Linear Systems
    Causal Systems
    Stable Systems

## Slide 3: 2 : Discrete-Time Systems
2.1 Discrete-Time System
A discrete - time system is a device or algorithm that operates on a discrete-time signal called the input or excitation according to some well defined rule, to produce another discrete-time signal called the output or response.
We say that the input signal x[n] is transformed by the system into a signal y[n], and express the general relationship between x[n] and y[n] as
(2.1)
yn Hxn

## Slide 4: yn H xn
H
x[n]
y[n]
Figure 2.1. Block diagram representation of a discrete-time System
where the symbol H denotes the transformation or processing performed by the system on x[n] to produce y[n] (see Fig 2.1)
x[n] y[n]
H
(2.1)

## Slide 5: 2.2 Block Diagram Representation
In order to introduce a block diagram representation of discrete-time systems, we need to define some basic blocks that can be interconnected to form complex systems.
  An adder : A system that performs the addition of two signal sequences to form another sequence, which we denote as y[n].
Note: It is not necessary to store either one of the sequences in order to perform the addition. In other words, the addition operation is memoryless.

## Slide 6
x1[n]
+
x2[n]
y[n] = x1[n]+x2[n]
x1[n] = {4, 5, -3}
x1[0]
x1[2]
sequence
at n=0 n=2
9, 0}
n=0 n=1 n=2
y[0]
y[2]
x2[n] = {-2, 4, 3}
n=0 n=2
Figure 2.2. Block diagram representation of an adder, x1[n] and x2[n] denote discrete-time input signals and y[n] denote a discrete-time output signals.

## Slide 7: (b) A constant multiplier: This operation simply represents applying a scale factor on the input x[n]. Note that this operation is also
a
memoryless.
multiplier
x[n]
y[n] = ax[n]
Figure 2.3. Block diagram representation of a multiplier. x[n] and y[n] denote discrete-time input and output signals respectively. a denotes a scalar multiplier.

## Slide 8: sequence
x[n] = {2, -5, 6, 8}; a = 0.1; y[n] ={0.2, -0.5, 0.6, 0.8}
at n=0 n=3 at n=0 n=3
(c) A Unit Delay Element : The unit delay is a special system that simply delays the signal passing through it by one sample.
If the input signal is x[n], the output is x[n-1]. In fact, the sample x[n-1] is stored in memory at time n-1 and
it is recalled from memory at time n to form y[n] = x[n-1].
Thus this basic building block requires memory

## Slide 9
The use of symbol T or z-1 to denote the unit of delay.
T
x[n]
y[n] = x[n-1]
Figure 2.4. Block diagram representation of a unit delay. T denotes the sampling period.

## Slide 10: Example:
Z-1
x[n]
y[n] = x[n-1]
unit delay
y[n] =
at n= -1; n=0; n=1
x[n] = {0, 1, 0, 5, 7, -2, -1, 0}
{0, 1, 0, 5, 7 , -2, -1}
y[0] y[1] y[2] … y[6]
{ y[n] = x[n-1]; y[0]=x[0-1]=x[-1]; y[1] = x[1-1]=x[0];…}

## Slide 11: Note: Normally a combination of adders, multipliers and unit delays form a complex discrete-time system.

## Slide 12
-20
-15
-10
-5 0
5
10
15
20
0
0.5
1
unit step
-20
-15
-10
10
15
20
0
0.5
1
unit step shifted left
-20
-15
-10
-5
0
5
10
15
20
0
0.5
1
-5 0 5
unit step shifted right

## Slide 13: 2.3 Difference Equations
A discrete-time system consisting of combinations of adders, multipliers and unit delays can always be described by a set of difference equations. The equations would be ordinary algebraic equations if no delays were present.

## Slide 14: Examples:
(a) y[n] = x[n-2]
T
x[n]
x[n-1]
T
y[n] = x[n-2]
T - Unit sample delay sampling period

## Slide 15: (b) y[n]  1 x[n]  1 x[n 1]  1 x[n  2] 2 4 4
T
x[n]
x[n-1]
T
x[n-2]
+
y[n]
0.5
0.25
0.25
0.5 x[n]

## Slide 16: (c) yn  xn 0.25 yn  1
y[n]
y[n-1] | T | 
+
0.25
x[n]
4
(d) y[n]   x[n  k]  x[n]  x[n 1]  x[n  3]  x[n  4]
k 0

## Slide 17: Example:
yn a0xn a1xn 1 b1y[n 1]
Draw a system implementation for the above difference equation.
y[n]
x[n]
a0
System 2
+
T
-b1
+
T
a1
v[n]
Feedforward Part Feedback Part Figure 2.5. Direct Form I structure
System 1

## Slide 18
We can write the above difference equation as a set of two equations

- system 1

- system 2
y[n]
x[n]
a0
System 2
+
T
-b1
+
T
a1
v[n]
Feedforward Part Feedback Part Figure 2.5. Direct Form I structure
System 1
yn  vn b1 yn  1
vn a0 xn a1xn 1

## Slide 19: y[n]
System 1 |  | System 2
v[n]
x[n]
System 2 |  | System 1
p[n]
x[n]
y[n]
Cascade structure
Figure 2.6. Two systems forming a cascade structure can be interchanged without affecting the final output signal.
Without changing the input-output relationship, we can reverse the ordering of the two systems in the cascade representation.

## Slide 20: 2.4 Classification of Discrete- Time Systems
In the analysis as well as in the design of systems, it is desirable to classify the systems according to the general properties that they satisfy.
For a system to possess a given property, the property must hold for every possible input signal to the system.
If a property holds for some input signals but for others, the system does not possess the property.

## Slide 21
General Categories are:
  Static systems
  Time - invariant systems
  Linear systems
  Causal systems
  Stable systems

## Slide 22
    Static Systems
      A discrete-time system is called static or memoryless if its output at any instant ‘n’ depends at most on the input sample at the same time, but not on past or
future samples of the input.
Example:
yn  axn
yn  nxn bx3 n
N
yn   xn  k 
k 0
Both are static or memoryless.
On the other hand, the systems described by the following input-output relations, such as
yn  xn 3xn  1
are dynamic systems or system with memory.

## Slide 23: 2.4.2 Time-invariant systems
A time-invariant system is defined as follows:
xn  n0 ⎯⎯ yn  n0 
H
where y[n] = H{x[n]}.
Specifically, a system is time invariant if a time shift in the input signal results in an identical time shift in the output signal.

## Slide 24: yn H xn nxn
Example: Determine if the system is time variant or time invariant.
This system is time variant, since
(2.7)
The response of this system to x[n-k] is
wn  nxn  k 
Now if we delay y[n] in (2.7) by k units in time, we obtain
yn  k   n  k xn  k 
 nxn  k  kxn  k 
yn  k  wn

## Slide 25: 2.4.3 Linear Systems
A linear system is defined as follows:
where a1 and a2 are arbitrary constants.
(2.8)
1 1 2 2
1 1 2 2
H
 a y n a y n
a x n a x n⎯⎯

## Slide 26: Example: Three sample averager
3
1 2
1 2
 ax1n bx2n
 ax1n 1 bx2n 1}
 [ay1n by2n]
H{ax n bx n}  1{ax n 1 bx n 1
3
xn⎯⎯H  yn
yn  1 xn 1 xn xn 1  H xn
The 3-sample averager is a linear system.

## Slide 27: yn   H xn   x 2 n 
Example:
n x n 
2
1
2
2 2
1
2 2
2
1 2
2
1
n  2 abx 
n  b x 
  ax n  bx n 
 a x 
H ax n  bx n 
which is not equal to ax 
2
2
2
1
n bx n
This system is nonlinear.

## Slide 28: Example :
yn  nxn  H  xn  H  ax1n bx 2 n  anx1n bnx 2 n
 ay1n by 2 n
The system is linear.

## Slide 29: 2.4.4 Causal systems
A system is said to be causal if the output of the system at any time ‘n’ depends only on present and past inputs, but does not depend on future inputs.
If a system does not satisfy this definition, it is called noncausal. Such a system has an output that depends not only on present and past inputs but also on future inputs.

## Slide 30: Example :
 Noncausal
 Causal
 Causal
yn  x n
yn  xn 3xn  4 Noncausal
yn  axn
yn  xn xn  1
{Let n = -1  y[-1]= x [1], the output at
n = -1 depends on the input at n = 1.}

## Slide 31
Discrete - time sequence is called
causal if it has zero values for n<0.
y[n]
Causal
& Stable
n
Figure 2.9. An example of causal discrete-time sequence.
n
3
2
yn    un

## Slide 32: 2.4.5 Stable Systems
A discrete signal x[n] is bounded if there exists a finite M such that
|x[n]| < M for all n.
A discrete - time system in Bounded Input-Bounded Output (BIBO) stable if every bounded input sequence x[n] produced a bounded output sequence.
If xnmax  A, then ynmax  B

## Slide 33: Example:
The discrete - time system
yn  nyn 1 xn, n  0
is at rest [i.e. y[-1]=0]. Check if the system is BIBO stable.

## Slide 34: n  0  y0  x0  1
If x[n]=u[n], then |x[n]|  1. But for this bounded input, the output is
n  1  y1  1y0 x1  2
n  2  y2  2 y1 x2  5
M M
Which is unbounded. Hence the system is unstable.